## Slide 1
Mobile Robot for Smart Restaurants
Group Members:
Muneeb Ahmad
Ahmed Saeed
Mohib Ahmed
Muhammad Zakriya
Supervisor:
Dr. Uzair Khaleeq uz Zaman
Co-Supervisors:
Dr. Anas Bin Aqeel
A/P Kanwal Naveed

## Slide 2
To Design & Construct a Mobile Line Following Robot that Can Automate the Job of a Waiter In a Restaurant Environment
Objective

## Slide 3
The Problem
3.5 Trillion USD Global Restaurant Industry [1]
Labor Shortages[2] - Prime Target for Automation
Opportunities to Reduce Cost and Increase Profits[3]
Improved Customer Experience[4]
Ordering, Payment & Serving are the Easiest & Most Beneficial to Automate

## Slide 4
Project Deliverables
Design & Build a Mobile Line Following Robot that is Able to Follow the Shortest path to a Destination (tables) and Avoid Collisions
1
2
4
Make it IoT Enabled so it can Send and Receive Data to and from Restaurant Staff
Ensure Ecosystem Integrability Through Software & Hardware Design as well as Industry Level Documentation
3
Make it Capable of Carrying Load (Food & Drinks) without Spilling Them Using Quick Interchangeable Carrying Trays

## Slide 5
Additional Accomplishments
Built An Ecosystem of Apps (Ordering, FoH Display, Remote Control) to Work Alongside the Robot as VAS
5
6
8
Used Cameras for Navigation Instead of a Sensor Based Approach; Enabled Robot to Map and Store the Restaurant Layout
Created a cloud Database for Restaurants to Digitize their Menus & Collect Valuable Trend Data
7
Studied Velocity, Acceleration & Braking Profiles to Ensure Robot Movement & Trajectory is Smooth and Safe

## Slide 6
Representative Environment

## Slide 8
Mechanical
Hardware

## Slide 9
Design Considerations
Based off Existing Designs
1
2
4
Mechanical Simulations on ANSYS to Determine Materials & Parameters for Load Carrying or High Stress Parts
Modular Custom Parts and In House Fabrication & Assembly
3
Design Factors Include Material availability, Safety, Cost, Strength/Load Carrying Capacity, Weight, Ease of Assembly and Aesthetics

## Slide 10
Existing Designs

## Slide 11
Our Design

## Slide 12
Design Breakdown

## Slide 14
Frame and Baseplate

## Slide 15
Frame and Baseplate

## Slide 16
Couplers and Wheels

## Slide 17
Coupler Deformation

## Slide 18
Coupler Stress

## Slide 19
Load Trays

## Slide 20
Load Trays Deformation

## Slide 21
Electrical
Hardware

## Slide 22
Electrical Design Highlights
Electronics are Mostly off the Shelf Components; Easy access and Replacement
1
2
4
Electrical Safety, Redundancy & Modularity Ensured
Dual Batteries With Built-in Charger & Charge Indicator
3
Selection & Acquisition of Electrical Hardware was done on the Basis of Mechanical Requirements

## Slide 23
Wiring Layout

## Slide 24
Connections Layout

## Slide 25
Motors and Drivers
Reduction Ratio | No Load Ratings |  |  | Loaded Ratings |  |  |  | Stall Ratings | 
 | Voltage | Speed | Current | Speed | Current | Torque | Power | Torque | Current
71 | 12 V | 112 RPM | 0.45 A | 90 RPM | 1.8 A | 10 kg cm | 21.6 W | 33 kg cm | 5 A

## Slide 26
Batteries
Voltage | Capacity | Max Current | Battery Timing | Charge Time
12 V | 28 + 3 Ah | 20A | 6-10 Hours | 4 Hours

## Slide 27
Controller
Controller | Clock Speed | Voltage | GPIO Pins | Analog Inputs | PWM Pins | UART / I2C / SPI | Wi-Fi | Bluetooth | Flash Memory | RAM | USB Interface | Price (Approx.)
Dual-core Tensilica LX6 | Up to 240 MHz | 3.3V | 34 | 18 (12-bit ADC) | Most GPIOs | 3 / 2 / 4 | Yes | Yes | 4MB (external) | ~520KB SRAM | Micro USB | $5–10

## Slide 28
Feature | ESP32 NodeMCU | Arduino Uno | Arduino Mega | RPi Pico
Microcontroller | Dual-core Tensilica LX6 | ATmega328P | ATmega2560 | Dual-core ARM Cortex-M0+
Clock Speed | Up to 240 MHz | 16 MHz | 16 MHz | 133 MHz
Voltage | 3.3V | 5V | 5V | 3.3V
GPIO Pins | 34 | 14 (6 PWM) | 54 (15 PWM) | 26
Analog Inputs | 18 (12-bit ADC) | 6 (10-bit ADC) | 16 (10-bit ADC) | 3 (12-bit ADC)
PWM Pins | Most GPIOs | 6 | 15 | All GPIOs
UART / I2C / SPI | 3 / 2 / 4 | 1 / 1 / 1 | 4 / 1 / 1 | 2 / 2 / 2
Wi-Fi | Yes | No | No | No
Bluetooth | Yes | No | No | No
Flash Memory | 4MB (external) | 32KB | 256KB | 2MB
RAM | ~520KB SRAM | 2KB | 8KB | 264KB
USB Interface | Micro USB | USB-B | USB-B | Micro USB
Price (Approx.) | $5–10 | $10–20 | $25–35 | $4–8

## Slide 29
Camera
Depth Sensing Range | Depth Resolution | RGB Resolution | FoV | Operating Systems | SDK Support
0.6 to 8 meters | 640×480 at 30 FPS | 1280×720 at 30 FPS | 60° horizontal × 49.5° vertical × 73° diagonal | Windows, Linux, Android | OpenNI, Astra SDK, ROS.

## Slide 30
Ecosystem Applications

## Slide 31
Ecosystem Highlights
A System of Supporting Flutter Apps Built around the Robot to act as VaS
1
2
4
A Dashboard App Installed in the Kitchen and Cashier Stations; Allows for tracking of Orders and their Updating their Statuses
A Remote Control App That Allows Manual Control Over the Robot from a Device by Authorized Users
3
An Ordering App That Can be Installed on Customers’ Phones, Tablets or Used Directly from the Robot
Databases that Allow Restaurants to Digitize their Menus and Collect Valuable Customer Data & Trends
5

## Slide 32
Ordering App

## Slide 33
Ordering App

## Slide 34
Dashboard App

## Slide 35
Dashboard App

## Slide 36
Remote Control App

## Slide 37
Remote Control App
Webcam Feed

## Slide 38
RC App Video
Webcam Feed

## Slide 39
Simulations & Navigation

## Slide 40
URDF & Kinematics
Created URDF Files from CAD Model, Calculated Forward & Inverse Kinematics of the Robot
1
2
Simulation First Approach Allowed for Easy Debugging and Testing Before Robot was Even Assembled
3
Simulated and integrated the Robot, Environment and Cameras in Gazebo Using ROS2 and the Kinematics

## Slide 41
Robot Model Using URDF & Kinematics

## Slide 42
Modeling the Environment

## Slide 43
Velocity Profiles

## Slide 44
URDF Code

## Slide 45
Kinematics Code

## Slide 46
Navigation
Created a Robust Line Identification and Tracking Algorithm Using OpenCV
1
2
4
Created a Mapping and Path Planning Algorithm
Used Depth Camera to Detect Obstacles and Avoid Collisions
3
Performed Junction Classification Using ArUco Markers

## Slide 47
Line Following Algorithm

## Slide 48
Junction Classification

## Slide 49
Mapping & Path Planning

## Slide 50
Collision Avoidance

## Slide 51
Line Identification

## Slide 52
Junction Identification

## Slide 53
Line Map

## Slide 54
Results &
Conclusions

## Slide 55
Testing Results
 | No. of Tests in Final Configuration | Successful Runs (Navigated & Delivered) | Partial Failures |  | Failed Runs
 |  |  | Navigated but did not deliver | Delivered but did not navigate | 
With Only Food | 10 | 9 | 0 | 1 | 0
With Only Drinks | 10 | 9 | 1 | 0 | 0
With Food & Drinks | 10 | 10 | 0 | 0 | 0
Total | 30 | 28 (93.33%) | 1 | 1 | 0

## Slide 56
Limitations
Scope Constraints; Lack of Realistic Testing Environment & Dependance On Structured Environment
1
2
4
Hesitation to Testing & Adoption, Especially by Local Restaurant Owners
Lack of Long Term Performance Data (Customer Trends, Battery Data, Wear & Tear Data)
3
Component Availability & Cost Issues, Delivery Issues from Foreign Suppliers

## Slide 57
Future Work
Transition To Full Autonomy Via SLAM
1
2
4
Multi Robot Integration & Fleet Management Operations
Design Optimizations; Charging Dock, PoS Integration, Moveable Trays, Voice Commands, Advanced UI & Language Support
3
Real Time Path Re-Planning & Dynamic Obstacle Avoidance

## Slide 58
Thank You

## Slide 59
Questions?